## Slide 1
BEE 208 — C++ PROGRAMMING
Transformer Load and
Efficiency Calculator System
Mid-Semester Practical Project Examination — Project Question 13
Department of Electrical/Electronic Engineering Accra Technical University — Faculty of Engineering Lecturer: Douglas Ayitey
Group Number: _____ Presented by: Group Members (see report.md)

## Slide 2
INTRODUCTION
Project Overview
A C++ console application that records transformer details, accepts multiple connected loads, calculates total demand, and reports whether the transformer is operating safely.
Records Details
Transformer name, rating, voltages and power factor
Accepts Loads
Multiple connected load types via a looped input
Calculates Demand
Total load, apparent load (kVA) and loading %
Reports Safely
Classifies status and warns of overload risk
WHY IT MATTERS
An overloaded transformer can:
Overheat
Lose efficiency
Trip protection devices
Suffer permanent damage
This system gives users an immediate, calculated answer — instead of a guess.
BEE 208 — Transformer Load and Efficiency Calculator System
2

## Slide 3
THE CHALLENGE
Problem Being Solved
Electrical users often connect several loads to a transformer without calculating the total demand this places on it — making it difficult to know its true operating condition.
Without a calculation tool, users cannot tell if a transformer is:
Underloaded
Operating normally
Near full capacity
Dangerously overloaded
Need for a Simple,
Reliable Tool
This project delivers a lightweight C++ programme that removes the guesswork and gives an immediate, calculated load status.
BEE 208 — Transformer Load and Efficiency Calculator System
3

## Slide 4
DIRECTION
Aim and Objectives
AIM Develop a C++ Transformer Load and Efficiency Calculator System that estimates a transformer's loading condition and clearly reports whether it is operating safely.
1
Identify input, processing, and output requirements
2
Write an algorithm for the calculator application
3
Write pseudocode for the application logic
4
Design a flowchart for the calculation process
5
Develop a working programme using functions & classes
6
Use loops to accept multiple connected loads
7
Use conditionals to classify transformer load status
8
Calculate total load, apparent load & loading %
9
Save the load report into a text file
10
Document the project using Markdown via GitHub
BEE 208 — Transformer Load and Efficiency Calculator System
4

## Slide 5
CAPABILITIES
Main Features of the Application
Transformer Details
Captures name, rated kVA, primary & secondary voltage, and power factor.
Multiple Loads
Loops to accept any number of connected load types with name, rating & quantity.
Input Validation
Rejects negative or non-numeric values and re-prompts the user automatically.
Automatic Calculations
Computes load power, total load, apparent load (kVA), and loading %.
Load Classification
Flags status as Lightly Loaded, Normal, Near Full Load, or Overloaded.
Report Generation
Displays a full report on screen and saves it to transformer_report.txt.
BEE 208 — Transformer Load and Efficiency Calculator System
5

## Slide 6
SPECIFICATION
System Requirements
Required Formulae
Load Power = Power Rating × Quantity
Total Load = Sum of all load powers
Apparent Load (kVA) = Total Load / (Power Factor × 1000)
Loading % = (Apparent Load / Rating) × 100
Load Status Classification
< 40%
Lightly Loaded
40% – 80%
Normal Operating Range
81% – 100%
Near Full Load
> 100%
Overloaded Warning
C++ Concepts Required: Input/Output • Variables & Data Types • Operators • Conditionals • Loops • Functions • Classes & Objects • Vectors • File Handling • Input Validation
BEE 208 — Transformer Load and Efficiency Calculator System
6

## Slide 7
DESIGN
Algorithm
1
Start & display project title
2
Enter & validate transformer details (loop until valid)
3
Enter number of connected load types
4
For each load: enter & validate name, rating, quantity
5
Calculate load power and accumulate total load
6
Calculate apparent load (kVA) and loading percentage
7
Classify load status using conditional statements
8
Display report and save to transformer_report.txt, then stop
BEE 208 — Transformer Load and Efficiency Calculator System
7

## Slide 8
DESIGN
Pseudocode
BEGIN
REPEAT
INPUT transformer name, rating, voltages, power factor
VALIDATE all values (reject negative / out-of-range)
UNTIL valid
INPUT numberOfLoads
totalLoadWatts = 0
FOR i = 1 TO numberOfLoads DO
INPUT loadName, powerRatingWatts, quantity
VALIDATE powerRatingWatts >= 0 AND quantity >= 0
loadPower = powerRatingWatts * quantity
totalLoadWatts += loadPower
END FOR
apparentLoadKVA = totalLoadWatts / (powerFactor * 1000)
loadingPercentage = (apparentLoadKVA / transformerRatingKVA) * 100
IF loadingPercentage < 40 THEN loadStatus = "Lightly Loaded"
ELSE IF loadingPercentage <= 80 THEN loadStatus = "Normal Operating Range"
ELSE IF loadingPercentage <= 100 THEN loadStatus = "Near Full Load"
ELSE loadStatus = "Overloaded Transformer Warning"
DISPLAY report
SAVE report TO "transformer_report.txt"
END
BEE 208 — Transformer Load and Efficiency Calculator System
8

## Slide 9
DESIGN
Flowchart
BEE 208 — Transformer Load and Efficiency Calculator System
9

## Slide 10
IMPLEMENTATION
C++ Concepts Used
Input & Output
cin / cout for all user interaction
Variables & Data Types
string, double, int throughout
Operators & Expressions
Arithmetic formulae for load & efficiency
Conditional Statements
if / else if for load status classification
Loops
for loop (loads), do-while & while (validation)
Functions
Modular member functions per responsibility
Classes & Objects
Transformer and LoadItem classes
Vectors
vector<LoadItem> stores all connected loads
File Handling
ofstream saves transformer_report.txt
Input Validation
Rejects negative & non-numeric values
BEE 208 — Transformer Load and Efficiency Calculator System
10

## Slide 11
IMPLEMENTATION
Explanation of the Code Structure
class LoadItem
Represents one connected load type. • inputLoadDetails() Prompts for name, rating, quantity • readValidatedDouble() Rejects negative/invalid numeric input • Getter functions Expose data for reporting
class Transformer
Performs all calculations & reporting. • setTransformerDetails() / validateTransformerDetails() • addLoadDetails() — loops through LoadItem objects • calculateApparentLoad() / calculateLoadingPercentage() • determineLoadStatus() — if/else if chain • displayTransformerReport() / saveReportToFile()
BEE 208 — Transformer Load and Efficiency Calculator System
11

## Slide 12
LIVE DEMO
Demonstration of the Programme
1
Compile: g++ -std=c++11 main.cpp -o transformer_calculator
2
Run the programme and enter transformer details
3
Enter the number of connected load types, then each load
4
View the calculated report displayed on screen
5
Open transformer_report.txt to confirm it was saved
BEE 208 — Transformer Load and Efficiency Calculator System
12

## Slide 13
EVIDENCE
Screenshots
Insert your own screenshots on this slide before presenting. Replace each placeholder box below with the matching image.
Input Screen
Terminal showing transformer & load prompts being answered
[ INSERT SCREENSHOT HERE ]
Output Screen
Terminal showing the full Transformer Load Report
[ INSERT SCREENSHOT HERE ]
File Output
Contents of the generated transformer_report.txt
[ INSERT SCREENSHOT HERE ]
BEE 208 — Transformer Load and Efficiency Calculator System
13

## Slide 14
REFLECTION
Challenges Faced
Mixing cin >> and getline()
cin >> leaves a newline in the buffer, which could cause getline() to read an empty line. Solved by clearing the stream to the next newline after every numeric read.
Balanced Input Validation
Validation had to reject bad values without forcing a full restart. Solved by validating each field individually in its own loop.
Correct Units in Formulae
Power factor as a decimal (not %) and watts-to-kVA conversion had to be exact, or the loading percentage — and its safety classification — would be wrong.
Coordinating a 10-Member Group
Keeping the algorithm, pseudocode, flowchart and code consistent across members required agreeing early on the shared class design and formulae.
BEE 208 — Transformer Load and Efficiency Calculator System
14

## Slide 15
REFLECTION
Lessons Learned
Stream State Matters
Careful tracing of cin's internal state, not just the visible output, is essential when combining formatted and line-based input in C++.
Validate Field-by-Field
Fine-grained validation (per field, not per record) produces a far friendlier and more robust user experience.
Design Before Code
Writing the algorithm, pseudocode and flowchart first kept the eventual C++ implementation focused and consistent.
Shared Design = Team Alignment
Agreeing on the Transformer/LoadItem class design early prevented the algorithm, code and docs from drifting apart.
BEE 208 — Transformer Load and Efficiency Calculator System
15

## Slide 16
LOOKING AHEAD
Future Improvements
Efficiency Calculation
Add (Output Power / Input Power) × 100 when input power data is available.
Multiple Transformer Records
Compare several transformers in one session using a vector of objects.
Historical Record-Keeping
Append timestamped reports instead of overwriting the file each run.
Graphical / Web Interface
Move beyond the console for easier use by non-programmers.
Data Export (CSV / PDF)
Export reports in formats easier to share or import into spreadsheets.
Configurable Thresholds
Allow the 40% / 80% / 100% classification bands to be adjusted.
BEE 208 — Transformer Load and Efficiency Calculator System
16